Note for mission
- default bounds are for when charruco is placed along xy with y being constant
- if charruco is placed along xy with x being constant, all one has to do is flip the parameter values. You can do that through argparse
- If charruco is placed along xy with y being constant, have both y_max and y_min be the same value but give y_max a negative value and y_min a positive value
- Do the same if the charruco is placed along xy with x being constant
- if we are too close or too far from charruco, adjust distance depending on what axis is constant.
- change number of segments and images with argparse
- default x and y bounds are for the drone to slightly go past the edge. If we need it to go more or less, again adjust respective bounds.
- Charruco measures 120x120 cm
- When we tell drone to move 1, that is equivalent to 1 m or 100 cm
- One can adjust the way the camera is facing with the use of “yaw_angle” interface. Adjust respectively
- One meter distance is perfect. If one is closer, drone senses that it is too close to the board, at least during simulation